THE FINE PUB GROUP – SCHEDULE OF DILAPIDATIONS

| PROPERTY: | The Fine Pub | LEASE: | 20 Year FRI |
| --- | --- | --- | --- |
|  | Anytown Road, Anytown |  |  |
| LESSEE (Outgoing): | Mr. Landlord | LESSEE (Ingoing): |  |
| Date of Inspection: | xxxx | Weather Conditions: | Overcast with Drizzle |
| General Description: | A 2-storey brick building with render and timber cladding under slated and felt roofs. Accommodation comprises at 1st floor full bathroom, office, 2 bedrooms and lounge. Ground floor has bar area, dining room, trade kitchen, ladies & gents toilets and cellar area. Externally is a timber barn under corrugated metal sheet roofing. |
| ITEM | LEASE CLAUSE | AREA | DEFECT | REMEDY | COST |
| External Areas |  |  |  |  |  |
| Front Elevation |  |  |  |  |  |
| Slated Roof | 3.7 | Complete Roof | Sagging Roof Slopes | Inspect roof timbers and repair as necessary |  |
| Slated Roof | 3.7 | Right Hand End | Slipped Slates | Re-fix slipped slates |  |
| Brickwork | 3.7 | Low level below windows | Missing pointing and lifting joints | Re-point in mortar to match existing and re-bed lifting bricks |  |
| Timberwork | 3.7 | Storm Lobby | Damaged and missing shiplap | Replace timber to match existing profile and decorate to match existing |  |
| Right Elevation |  |  |  |  |  |
| Rainwater Goods | 3.7 | Rainwater Pipe | Discharge Shoe buried in ground | Adjust Rainwater shoe to finish above ground level and into rainwater drainage system |  |

THE FINE PUB GROUP – SCHEDULE OF DILAPIDATIONS

| PROPERTY: | The Fine Pub, Anytown Road, Anytown | LEASE: | 20 Year FRI |
| --- | --- | --- | --- |
| Date of Inspection: | xxxx | Weather Conditions: | Overcast with Drizzle |
| ITEM | LEASE CLAUSE | AREA | DEFECT | REMEDY | COST |
| Rear Elevation |  |  |  |  |  |
| Rainwater Goods | 3.7 | Complete System all levels | Blocked and misaligned | Clean out complete system, realign to falls and leave clear and free running |  |
| Slated Roof | 3.7 | Lean-to over Kitchen | Numerous slipped and damaged slates | Thoroughly overhaul replacing all damaged slates, fixing all slipped slates and leaving all sound |  |
| Felted Roof | 3.7 | Over Toilets | Accumulated debris | Remove all plant debris and leave clean |  |
| Cement Render | 3.7 | Adjacent to Kitchen Door | Damaged sections | Properly remove all loose render and renew to finish flush with surrounding areas. Decorate on completion |  |
| Timberwork | 3.7 | Toilet Block soffit | Rotting plywood | Remove damaged sections and renew to match. Decorate to match existing |  |
| Decorations | 3.10.1 | All surfaces Render & Timber | Peeling and discoloured surfaces | Decorate all to comply with lease clauses |  |
| Left Elevation |  |  |  |  |  |
| Decorations | 3.10.1 | Timber Boarding | Bare timber in areas | Decorate all with Timber preservative paints |  |

THE FINE PUB GROUP – SCHEDULE OF DILAPIDATIONS

| PROPERTY: | The Fine Pub, Anytown Road, Anytown | LEASE: | 20 Year FRI |
| --- | --- | --- | --- |
| Date of Inspection: | xxxx | Weather Conditions: | Overcast with Drizzle |
| ITEM | LEASE CLAUSE | AREA | DEFECT | REMEDY | COST |
| External Barn |  |  |  |  |  |
| Corrugated Metal | 3.7 | Main Roof | Damaged sections | Inspect roof structure and repair with replacement of damaged corrugated sheets to match existing |  |
| Decorations | 3.10.1 | All vertical surfaces | Undecorated | Decorate all with Timber preservative paints |  |
| Internal Areas |  |  |  |  |  |
| Electrical | 3.7 | 1st Floor Bathroom | No light pullcord | Install lighting pullcord |  |
| Decorations | 3.10.2 | 1st Floor Bathroom | Ceiling Hatch | Decorate ceiling Hatch |  |
| Ironmongery | 3.7 | 1st Floor Bathroom | No Door Lock | Install Door Lock |  |
| Ironmongery | 3.7 | 1st Floor Hallway | Missing window lock | Install window locking device to match existing |  |
| Plasterwork | 3.7 | Staircase at 1st floor level | Damaged and Damp | Investigate dampness and rectify. Repair damaged plaster to finish flush with surrounding areas. |  |
| Plasterwork | 3.7 | Ground floor ceiling in lobby under hot water cylinder | Hole in ceiling | Repair hole and decorate to match existing |  |
| Plasterwork | 3.7 | Trade Kitchen ceiling | Damaged areas | Repair and redecorate |  |

THE FINE PUB GROUP – SCHEDULE OF DILAPIDATIONS

| PROPERTY: | The Fine Pub, Anytown Road, Anytown | LEASE: | 20 Year FRI |
| --- | --- | --- | --- |
| Date of Inspection: | xxxx | Weather Conditions: | Overcast with Drizzle |
| ITEM | LEASE CLAUSE | AREA | DEFECT | REMEDY | COST |
| General Items |  |  |  |  |  |
| Decorations | 3.10.1 & 3.10.2 | All Levels all Surfaces not previously mentioned | As per lease clauses | Carry out Decorations |  |
| Electrical System | 3.23.2 | Complete premises | No Certificate on Site | Provide NICEIC certificate of compliance |  |
| Electrical Equipment | 3.11.1 | All Trade appliances | No PAT certification visible | Provide certification of compliance with Portable Appliance Testing for equipment. |  |
| Asbestos Survey | 3.11.1 | Complete premises | No survey to establish the presence of any Asbestos | Provide Type 2 survey to comply with Control of Asbestos at Work Regulations 2002 |  |
| Disability Discrimination Act | 3.11.1 | Trade Areas including Toilet Facilities | No Audit Survey available | Provide audit survey report to indicate compliance with Act |  |
| Gas Installation | 3.11.1 | Complete Gas Installation and Appliances | No Landlords Gas Inspection Certificate available | Supply “Corgi” Gas Inspection Certificate for Installation and Appliances |  |
| Drainage System | 3.7 | Complete waste management system | No records of service or maintenance | Provide records of servicing and maintenance contracts |  |